offset table vfp 25‘ mc                                                           fritz.roth@proadesign.com  dec 12 - 2004

25’   loa       22’8         20’       17’4“         14’8“        12’         9’4“          6’8“           4‘       16“      Center of hull

the station location from the center length wise of the main hull  - counting both sides

12‘6“       11‘4“       10’         8’8“        7’4“          6’           4‘8“          3’4“            2’            8“            C

the station location from the center length wise of the main hull - one side only

bow

bow            #8            #7            #6           #5            #4           #3            #2           #1           #0   = >  #C

the  distance of the stem  from the #8 station   .....  station numbers for the main hull

14“ >        3“1/4        5“1/2      7“3/8         8“3/4          9“3/4      10“1/4       10“5/8    10“7/8       11“         +18“

13“ >      3“3/16      5“7/16    7“5/16     8“11/16     9“11/16    10“3/16    10“9/16   10“13/16   10“15/16    +12“

11“ >      2“5/8        4“7/8        6“3/4        8“1/8         9“1/8          9“5/8       10“       10“1/4       10“3/8        +6“

8“   >      2“5/16      4“3/16      6“            7“3/16       8“3/8          8“5/8        9“3/16   9“7/16       9“9/16       +2“

4“   >      1“3/8        3“1/2       5“1/4        6“1/2        7“11/16       8“1/4        8“11/16   8“7/16      9“              wl

1“5/8      4“1/16      5“11/16      6“3/4         7“3/8         7“7/8       8“1/16     8“1/8          -2“

“3/8       3“1/4        5“              6“1/4          6“7/8       7“5/16      7“5/8      7“11/16       -3“

2“             4“              5“3/6          6“1/16       6“3/8       6“5/8      6“3/4         - 4“

3/8“  <  keel  off center                        1“5/8           3“7/16        4“7/16     4“15/16     5“3/16     5“5/16       - 5“

making  the keel / stem  ¾ “  or 20mm                                      1“           2“           2“1/2       2“3/4         - 6“

as well as the stem up to +6“ from the wl

then in addition on each side one more layer of foam

depth below wl       3“        4“1/2       5“1/4       5“7/8         6“1/8         6“5/16       6“7/16       6“1/2“

dimension at the stations below the wl    - there will be a keel plank going on there on top

but not on the stem  - only on ist side ...